## Slide 1: Intelligent Home Security with NVIDIA Jetson
Paul DeCarlo
Sr. Cloud Advocate
@pjdecarlo Deck available @ https://aka.ms/IntelligentHomeSecurity

## Slide 2: Hardware
NVIDIA Jetson Device (Nano)
7-Inch Color Monitor
HDMI Splitter

## Slide 3: DeepStream SDK IoT Edge Module

## Slide 4: Deploy modules using Azure IoT Edge
Built on container technology as ‘modules’
Modules support Python, NodeJS, .Net Core, Java, & C
Low-latency AMQP / MQTT data transport
Operate in offline / intermittent network conditions
Supports Linux X64 | ARM32/64 , Windows X64
OSS and available @ https://github.com/Azure/iotedge

## Slide 5: IoT Edge Camera Tagging Module
Capture contextual images at site of deployment
Push images to CustomVision.AI or Blob Storage (Local and Cloud)
Automate via Direct Methods
Facilitate ML Ops with automated sampling and iterative training

## Slide 6: Train and export Model from CustomVision.AI

## Slide 7: Object Detection data overload
Messages are produced extremely fast (as high as 30 per second depending on algorithm and batch configuration options)
Great for reacting to real-time events at the edge
Way too much data to for summary reporting

## Slide 8: Flatten, Aggregate, and summarize detections
Stream Analytics Job deployed at Edge
Parse object detections into flattened list
Remove duplicates and count objects by @timestamp
Floor the average count over a 30 second tumbling window

## Slide 9: Example summarized payload
{"count":1.0,"sensorId":"Yard","object":"Car","@timestamp":"2020-05-07T13:37:00.0000000Z"}
{"count":1.0,"sensorId":"Street","object":"Car","@timestamp":"2020-05-07T13:37:00.0000000Z"}
{"count":1.0,"sensorId":"House","object":"Person","@timestamp":"2020-05-07T13:37:00.0000000Z"}
1 Car in the Yard, 1 Car in the Street, 1 Person in the House

## Slide 10: Modeling Data into TSI
Partition data by iothub-connection-device-id / sensorid
Create Hierarchy to organize sensorId by location
Create ObjectDetectionType to report detections of interest
Easily visualize / summarize data over time intervals

## Slide 11: Forward Streaming Data to Power Bi
Select all incoming summarized data from IoT Hub
Forward into Power BI Output Sink

## Slide 12: Create a Power BI report
Report based on live streaming data updated every 30 seconds as messages flow into IoT Hub
Slice based on any combination of time, sensorid, or object
Summarize data at a glance

## Slide 13: Publish Dashboard and ask questions

## Slide 14: REsources
This PowerPoint Presentation
  https://aka.ms/IntelligentHomeSecurity
Introduction to the Azure IoT Edge Camera Tagging Module
  https://aka.ms/CameraTaggingIntro
IoT Edge at GTC Digital 2020
  https://aka.ms/EdgeAtGTC
Visual Anomaly Detection using NVIDIA Deepstream IoT (WorkShop)
  https://aka.ms/DeepStreamOnEdgeWorkshop
DeepStream edge-to-cloud integration with Azure IoT
  https://aka.ms/DeepStreamIoTEdgeWebinar

## Slide 15: Detailed repro instructions @
aka.ms/intelligentvideoanalytics